## Slide 1: Volta-7 ATE Test Coverage Review
Author: Emma White, Test Engineer Lead
Platform: Advantest V93000 (SmarTest 8)
Date: April 24, 2026

## Slide 2: Title & Test Engineering Overview
Title: Volta-7 ATE Test Coverage and Execution Optimization Review
Author: Emma White, Test Engineer Lead
Target Application: High-Volume Wafer Sort & Final Package Test
Tester Platform: Advantest V93000 PS1600 Mixed-Signal Direct Probe / Socket
Key Milestones:
  Completed fault simulation coverage across digital logic, memory, and analog blocks.
  Optimized test execution time from 6.40s down to 3.14s (beating 3.20s budget).
  Integrated tri-temperature screening (-40°C, +25°C, +125°C) for automotive qual.
Notes: Good afternoon. This readout details our final production test program release for Volta-7 on the Advantest V93000 platform.

## Slide 3: Fault Simulation & Test Coverage Breakdown
Digital Core & Peripheral Coverage:
  Stuck-at Fault Coverage: 99.42% (Target: >99.0%). Total faults graded: 1,420,890.
  Transition Delay Fault Coverage (At-Speed Scan): 96.81% (Target: >95.0%).
  Bridging Fault Coverage: 94.20%.
Embedded Memory & Mixed-Signal Coverage:
  Embedded Flash & SRAM BIST: 100% coverage with 13N March C+ and checkerboard algorithms.
  Analog BIST & Trims: Bandgap, internal RC oscillator, and high-voltage charge pump trimmed to <0.5% tolerance.
  High-Speed IO: Full functional loopback on CAN-FD (5 Mbps) and LIN (20 kbps) channels.
Notes: Our fault simulation numbers exceed industry automotive baselines, ensuring defect screening down to single-digit Defective Parts Per Million (DPPM).

## Slide 4: Initial vs Optimized Test Time Breakdown
Execution Time Evolution:
  First Program Prototype (Jan 19): 6.40 seconds (Severely unoptimized).
  Rev 1.0 Release (Feb 23): 3.82 seconds (Functional, but exceeds 3.20s target).
  Rev 1.2 Final Production (Apr 19): 3.14 seconds (PASSED TARGET).
Key Optimization Breakthroughs:
  Concurrent ADC Sampling: Parallelized ADC0 and ADC1 linearity test patterns (-350 ms).
  Scan Vector Compression: Applied SmartBIST pattern compaction (-180 ms).
  Streamlined OTP Verification: Eliminated redundant read cycles during non-volatile ID burn (-150 ms).
Notes: Shaving test time from 3.82s to 3.14s saves FastChip over 180,000 annually in backend tester time and guarantees Penang test floor capacity.

## Slide 5: Tester Platform & Multi-Site Parallelism
Hardware Configuration:
  Tester: Advantest V93000 with 32-channel DC Scale and high-speed digital PS1600 pins.
  Wafer Sort: Dual-DUT probe card (2-site parallel test) with ceramic blade needle interface.
  Final Package Test: Quad-site (4-DUT parallel) test socket board with Kelvin contactors.
Parallel Test Efficiency (PTE):
  Wafer Sort PTE: 96.4% efficiency across 2 sites.
  Final Test Quad-Site PTE: 94.8% efficiency across 4 sites.
  Zero cross-talk or ground-bounce interference observed during simultaneous multi-site scan bursts.
Notes: Our quad-site final test hardware delivers tremendous throughput, capable of testing over 4,500 units per hour per tester.

## Slide 6: Production Test Flow & Guardbanding Sign-off
Automotive Production Screening Flow:
  Step 1: Wafer Sort (Austin / Penang): Room temperature (25°C) screening + wafer map scrap defect flagging.
  Step 2: Backend Assembly: Mold into wettable-flank QFN-48 package.
  Step 3: Tri-Temp Final Test (Penang Backend):
    Insertion 1: Hot Test (+125°C) — 100% functional, analog trim, and high-temperature leakage.
    Insertion 2: Cold Test (-40°C) — At-speed scan timing, low-temperature charge pump regulation.
Statistical Guardbanding: Limits tightened by 6σ based on 50,000-unit CPK characterization distributions.
Sign-off: Emma White (Lead Test Eng) | Anna Becker (Quality Mgr).
Notes: This tri-temp screening flow guarantees zero escapes to NovaDrive Motors. Test program is locked and ready for commercial production.